## Slide 1: Generating the Ollie Manoeuvre
Trajectory Optimization and its Application to Skateboarding
By Nicholas Anderson

## Slide 2: The Ollie
https://www.youtube.com/watch?v=OrOZxOTIv-g
Notes: The ollie is the fundamental manoeuvre in skateboarding.
The pop, slide, apex, landing

## Slide 3: The Ollie
Frederick et al., 2006
The Standing Ollie (SO)
The Rolling Ollie (RO)
The Ollie Down (OD)
The Ollie Up (OU)

## Slide 4: Trajectory Optimization
In its application to skateboarding…
Find input forces and torques
Perform the ollie
Satisfy constraints
Minimize cost/objective function
Notes: It’s a special way of simulating motion where you don’t know how the motion is performed or the forces involved.
In its application to skateboarding, the trajectory optimization problems seeks to find a set of input forces and torques applied by the skateboarder on the skateboard in order to perform the ollie. The solution should satisfy a set of constraints such as … while minimizing the applied forces and torques.

## Slide 5: Trajectory Optimization in Motion Studies
Motion analysis
Injury identification and prevention
https://q1065.fm/skateboaders-huge-wipeout-prove-helmets-work-video/
https://www.ncbi.nlm.nih.gov/pubmed/17509598
Notes: Motion studies – understand the key factors that influence motion. E.g. the effect of a high jumper’s arms on the jump height
Injury identification and prevention – understanding the forces involved on a skateboarder performing an ollie
Motion studies into skateboarding are sparse, even though skateboarding has been included in 2020 Tokyo Olympics.
Therefore, the aim of this project was to replicate the motion of the ollie manoeuvre and the ground reaction forces acting on the skateboard wheels.

## Slide 6: Methodology
Model the System
Formulate Trajectory Optimization Problem
Implement & Test
Notes: Iterative. Start with low complexity model of system, formulate traj opt problem, implement and test.
Increase complexity until model encapsulates the key dynamics of the real-bodies.

## Slide 7: Modelling
Skateboarder
Skateboard
Euler-Lagrange Method
→
https://sidewalkmag.com/skateboard-tricks/beginner-tricks/how-to-ollie-sidewalk-basics.html/2
Notes: Skateboarder – open kinematic chain of rigid-links. Torso, pelvis and legs. Legs are modelled as prismatic joints.
Skateboard – A single rigid link with massless wheels and wheel bearings. Negligent friction at wheels.
Using the Euler-Lagrange method, the EOMs of the system were calculated.

## Slide 8: Modelling
https://sidewalkmag.com/skateboard-tricks/beginner-tricks/how-to-ollie-sidewalk-basics.html/2
The foot-deck contact
Normal force – Inelastic
Friction force – Coulomb friction
The wheel-ground contact
Normal force – Inelastic
Negligible friction
The tail-ground contact
Elastic “pop”
The variable ground
Step-up or step-down
Notes: Various multi-body contacts in the system which occur at dynamics positions.
Isolated and bouncing ball model used for development

## Slide 9: Formulating the Problem - Contacts
The Hybrid Dynamics Method
Scheduled elastic or inelastic collisions
Map states before and after a condition is met
Notes: Two contact handling methods that were used:
Hybrid dynamic method which is for elastic and inelastic collisions.
Map the velocity of the skateboard tail before and after the collision using the coefficient of restitution
Drawback - scheduled

## Slide 10: Formulating the Problem - Contacts
The Contact-Implicit Method
Unscheduled inelastic collisions and friction
Defines a complementary relationship between two events of the form:
Events cannot occur at the same time
Notes: Contact-implicit for inelastic collisions and Coulomb friction. The pro for this method is unscheduled.
Complementary relationship between two events, forcing them to not occur at the same time.

## Slide 11: Formulating the Problem
Total Applied Force Squared
Total Applied Torque Squared
Penalty Variable
THE OBJECTIVE FUNCTION
CONSTRAINTS
Some pseudo code examples…
Notes: The constraints and objective function of the problem could now be specified. Examples of the constraints imposed on the system are …
The objective function was chosen to minimize the total force and torque applied by the skateboarder. A further penalty variable was added to increase the feasibility of the complementary relationships.

## Slide 12: Development of Contacts – pt 1
Tail-Ground (elastic)
Wheel-Ground (inelastic)
Low-Step
High-Step
Notes: Each of the contacts would now be isolated and tested.
Using the bouncing ball, the tail-ground contacts and wheel ground contacts were isolated and developed. The low-step and high-step tests were also incorporated into the tests.

## Slide 13: Development of Contacts – pt 2
Foot-Deck: Normal Force
Foot-Deck: Friction
Notes: Then, the foot-deck contacts involving a normal reaction force and a friction force were isolated and developed.

## Slide 14: Model Evolution
Notes: Now that the contacts within the system have been developed, the skateboard and skateboarder models could be developed from a low complexity model involving forces acting on the skateboard, to a higher complexity model with the skateboarder modelled as a biped. I call this diagram, the “model evolution”

## Slide 15: Development – Design 1
Fixed Applied Forces
Dynamic Applied Forces
Notes: The first stages of development involved applied forces on the skateboard, initially fixed in position and then dynamic along the deck of the skateboard.

## Slide 16: Development – Design 2
Monopod and Applied Force
Two Monopods
Notes: The next design iteration included monopods on the skateboard which represented the skateboarder’s legs. At this stage, it was promising (and exciting) to see that, not only can the monopod lift its feet off the skateboard, but it is also able to slide it’s foot up the skateaboard.
Since these designs were successful, the final biped model could be formulated into the problem. The results were as follows:

## Slide 17
Notes: A 0,5m standing ollie

## Slide 18
Notes: 0,5m Rolling ollie

## Slide 19
Notes: 0,36m ollie down. It should be noted that the characteristic “pop” was removed as it appeared that skateboarders often did not use this for small step-downs.
Under the time constraints of this project, the OU could not be successfully implemented.

## Slide 20: Comparison of SO Trajectory

## Slide 21: Comparison of SO Trajectory

## Slide 22: Comparison of RO Trajectory

## Slide 23: Ground Reaction Force Profiles
Rolling Ollie Take-Off
Ollie Down Landing

## Slide 24: Ground Reaction Force Profiles
Rolling Ollie Take-Off
Ollie Down Landing

## Slide 25: Peak Ground Reaction Forces
Take-Off
Landing

## Slide 26: Conclusions
Unscheduled multi-body contact method was successfully implemented
Successfully replicated the motion of the ollie
General shape of GRF profiles bare basic resemblances
Magnitude of GRF profiles different
The model has the required complexity to replicate the ollie motion, but needs further development to improve accuracy of the simulated ground reaction forces.

## Slide 27: Recommendations for Further Development

## Slide 28: Not quite so impressive…